## Slide 1: Code Sprint 2023: MUDDI GML Writing with FME CityGML3 Tests
Dean Hintz
Trent Kading

## Slide 2
Input data: Burnaby Sanitary Sewer - GeoJSON

## Slide 3
FME Workflow: Burnaby GeoJSON to MUDDI GML

## Slide 4: Data Transform Process
Read GeoJSON
Generate and convert timestamps to ISO format
Map attributes from source to MUDDI schema
Create missing attributes, including all required attributes
Create parent network features
Generate gml_ids from UUIDs and gml_parent_ids to associate network elements with parent networks
Set geometry property
Write MUDDI GML using ApplicationSchema.xsd from Interactive Instruments
Note: GML writer - Import Schema:
https://community.safe.com/s/article/gml-writing-with-application-schemas

## Slide 5: Validation Errors
XML Validation: Error in ‘./MUDDIgmlTest.xml' on line 16, column 16: 'element 'geometry' is not allowed for content model '(metaDataProperty*,description?,descriptionReference?,identifier?,name*,boundedBy?,location?,businessContact,certification?,dataOwner?,dataOwnerUniqueID?,dataProviderUniqueID?,dataProvider,dataSensitivityLevel?,dateDataCollected?,dateOfLastStatusChange?,description?,featureType?,guidance*,horizontalCRS,measurementUnits?,operationalStatus?,originalDateDataCollected?,systemID,systemLoadDate,version?,objectID,verticalCRS?,recordID,encloses?,enclosedBy*,centroidXYZ?,depth?,depthMethod?,enhancedMeasures?,enhancedMeasuresProximity?,horizontalAccuracy?,horizontalMeasurementMethod?,intendedPermanence?,emergencyContact,localeReference*,locationType?,assetName?,assetOwner?,assetOwnerID?,operator?,qualityLevel?,undergroundStatus?,material?,verticalAccuracy?,colour?,azimuth,container?,dateOfInstallation?,insideHeight?,insideLength?,insideWidth?,isAuxiliary?,isCathodicProtected?,isEncased?,isNPS?,outsideHeight?,outsideLength?,outsideWidth?,protectiveMaterial?,utilitySubType?,utilityType?,wallThickness?,siteOf?,accessoryType,associatedAssets*,hasAccessory?,accessType?,numberOfCovers?,geometry)‘’
Required: businessContact, dataProvider, horizontalCRS, objectID, recordID, emergencyContact, accessoryType, geometry

## Slide 6
Output: Burnaby Sewer MUDDI GML

## Slide 7
Output:
MUDDI GML: Burnaby Sewer
3D line geometry for network links interpolated from source start, end heights

## Slide 8
Output:
MUDDI GML: Burnaby Sewer
xlink_href to associate edges with nodes for topology

## Slide 9: CityGML3
Montreal CityGML2 to CityGML3
IFC to CityGML3 - duplex

## Slide 10: Montreal CityGML2 to 3: FME Workflow

## Slide 11: Montreal CityGML2 to 3: Output

## Slide 12: IFC Input: Duplex_A_20110907.ifc

## Slide 13: IFC to CityGML3 FME workflow (Dave Campanas)

## Slide 14
IFC to CityGML3 FME workflow pt1

## Slide 15
IFC to CityGML3 FME workflow pt2

## Slide 16: IFC to CityGML3 FME workflow pt3

## Slide 17: CityGML3 output: BuildingConstructiveElement

## Slide 18: CityGML3 output: BuildingRoom with generic attributes

## Slide 19: CityGML3 output: BuildingRoom with generic attributes

## Slide 20: Conclusions
MUDDI with FME
Wrote to MUDDI GML
Captured multiple geometry types: points, lines, polygons, 2d,3d
Populated complex schema elements including topology xlink_hrefs
CityGML3 with FME
Converted CityGML2 to 3 but still losing appearances (support coming with CityGML3 writer in 2024 Q1
IFC to CityGML3 – now able to store IFC spaces as rooms and support a range of other new CityGML3 feature types and properties (Story)
Read output back in with new CityGML3 reader

## Slide 21: Thank you
dean.hintz@safe.com
www.safe.com/fme