## Slide 1: Clemens Portele | interactive instruments Panagiotis (Peter) A. Vretanos | CubeWerx Inc. 09-OCT-2025
OGC Features and Geometries JSON (JSON-FG)

## Slide 2: About JSON-FG
Intentional limitations exist in GeoJSON
  Restricted to WGS 84 (longitude/latitude) as Coordinate Reference System
  Points, line strings and polygons – no support for 3D, non-linear interpolation or measures
  Supports spatial, but not time
  No feature type concept, no information about the schema
JSON-FG specifies GeoJSON extensions to address these constraints
  Avoid edge cases, focus on capabilities that are useful for many spatial experts
  Specify as a superset of GeoJSON: Valid JSON-FG is also valid GeoJSON
  Extensions:
    Additional JSON members in feature collections, features and geometries
    Additional geometry types
  JSON Schema is used to formally specify the JSON-FG syntax

## Slide 3: Requirements class overview
Mandatory extensions (Core):
  Coordinate Reference Systems other than WGS 84
  The ability to encode temporal characteristics of a feature
  A statement to which JSON-FG conformance classes a JSON-FG feature collection, feature, or geometry conforms to
Optional extensions specified in additional requirements classes:
  Support for polyhedra as geometry types
  Support for prisms (extruded geometries) as geometry types
  Support for circular arcs, compound curves, and curve polygons as geometry types
  Support for measure values in coordinates
  The ability to declare the type and the schema of a feature

## Slide 4: An example - three airports in the UK
“conformsTo”:
  declaration of the supported conformance classes
“place”:
  a primary feature geometry that is not a Simple Feature geometry or not in WGS 84 longitude/latitude
“coordRefSys”:
  Coordinate reference system of the geometry in “place”
“geometry” (from GeoJSON):
  a primary feature geometry that is a Simple Feature geometry and in WGS 84 longitude/latitude (optional, if “place” is provided)
“geometryDimension”:
  hint about the geometry types used (0 = points)
“featureType”, “featureSchema”:
  Information about the type of a feature and the logical schema of the features of that type

## Slide 5: Another example – a road accident in Germany
“time”:
  a primary temporal information

## Slide 6: Technical changes since the Public Comment Period
Improvements
  Use “application/geo+json” as the media type, do not register a JSON-FG media type
    Supports GeoJSON clients that access JSON-FG documents over HTTP
    Specification of three GeoJSON profiles
  Geometries are also first class JSON-FG objects, not just features and feature collections
    Allows, for example, reuse of the geometries in future versions of CQL2-JSON
  Updated JSON Schemas to test more requirements through JSON Schema validation
New capabilities
  Added support for circular arcs – plus curves and surfaces with arcs
  Added support for measure (M) coordinates
Removed from scope
  The permission to use non-Euclidean metrics, in particular ellipsoidal metrics
    This would break GeoJSON, which requires Euclidean metrics for GeoJSON geometry types
    GeodesicString has been added as an example of a geometry extension
  Support for CURIEs
    CURIEs add overhead to parsers, but are not an advantage to writers

## Slide 7: Circular arcs
New geometry types CircularString, CompoundCurve, CurvePolygon, MultiCurve, MultiSurface
JSON representation based on WKT of the geometry types with the same name from SQL/MM
  Following the same conventions as GeoJSON – the use of “coordinate” arrays, a “type” member and a “geometries” array for collections of geometries
Widely implemented in spatial databases
Multiple requests for support

## Slide 8: Measure (M) coordinates
GeoJSON supports more than three coordinates in a position, but discourages non-spatial coordinates
Multiple requests for support
M coordinates are supported in WKT and widely supported in spatial databases
“measures”
  Used to declare the use of M coordinates in geometries
  The meaning of the X/Y or X/Y/Z coordinates is declared through the “coordRefSys” member
  “unit” and “description” provide metadata (optional)
Only in “place”, not in “geometry”

## Slide 9: GeoJSON profiles
A GeoJSON document should use the “application/geo+json” media type
A profile specifies “additional semantics (constraints, conventions, extensions) that are associated with a resource representation, in addition to those defined by the media type” [RFC 6906]
JSON-FG specifies three profiles for use in Web APIs such as those implementing OGC API Features
  RFC 7946 ("rfc7946"): GeoJSON as specified in RFC 7946
  JSON-FG ("jsonfg"): JSON-FG as specified in this Standard
  JSON-FG with improved support for GeoJSON readers ("jsonfg-plus"): JSON-FG with a geometry in the "geometry" member
Profiles are requested via a ”profile” query parameter (one or more profiles)
  Example: ...&profile=jsonfg-plus,rel-as-uri

## Slide 10: HTTP-Response with Profile “rfc7946”

## Slide 11: HTTP-Response with Profile ”jsonfg-plus”

## Slide 12: Implementations
Multiple implementations of the previous draft (v0.2)
  Servers/APIs
  Map clients
  Converters (including GDAL)
  Validators (including the OGC Checker by Geonovum)
Tested and used in multiple code sprints
Changes since v0.2 that may affect current implementations (ignoring new capabilities):
  Use of “application/geo+json” as the media type, use of GeoJSON profiles
  Removal of CURIEs
  New version  new Conformance Class URIs
At least two implementations will be upgraded, including support for the new capabilities, in parallel to the approval process

## Slide 13: Sprint goals
Outreach
  Make people in the “geo” space aware of this standard
  All the nice things about GeoJSON with added “spice” to handle more advanced use cases
Test the new things we added
  Circular arcs
  Measure coordinates
  Profile support

## Slide 14: Dependency on OGC API – Features – Part 5: Schemas
Schemas referenced by a “featureSchema” member are logical schemas that conform to OGC API – Features – Part 5: Schemas
Part 5 is currently still a draft
Close to finalization, should be submitted to the TC in a few weeks
Delay JSON-FG publication until the vote of Part 5 has passed?

## Slide 15: THANK YOU
www.ogc.org